sound & tactile sensing
sound & tactile sensing

---
why combine tactile & sound sensors?
why combine tactile & sound sensors?
- applications are very different
- but both are (usually) pressure transducers
- big difference is the frequency range
  - pressure: DC - ~1 Hz
  - tactile: ~ 0.1 Hz - ~ 1000 Hz
  - sound: ~10 Hz - ~ 10 MHz (or more)
- typical devices are electromechanical
  - similar – or the same – transducer
    is used as both the transmitter & the receiver

---
- pressure is force per unit area
- almost all force – or pressure – sensing technologies involve …
  - a mechanical deformation under load
  - transduction-to-electrical to measure it
the main exception is for measuring gas pressure under near-vacuum conditions
  - then it is typically done at a microscopic level
    - cooling rate of an electrically heated filament
    - ion current produced by an electron current
    - drag on a magnetically-suspended rotor
  - these are really density measurements, translated into pressure via P V = n R T

---
reading (Fraden)
reading (Fraden)
Section 3.10, Sound
  - understand Equation 3.105
  - be happy with Table 3.3
- Section 6.1, Ultrasonic Sensors
- Section 7.6, Ultrasonic Sensors
- Chapter 9, Force, Strain, Tactile
- Chapter 10, Pressure
- Chapter 12, Acoustic

---
topics we will cover
topics we will cover
- the jargon of sound measurement (briefly)
- wave packets & consequent issues
- matched filter determination of ToF
- problem: beam width & specular reflection
- survey of sonar transducers
- the “strange” behavior of piezoelectrics
- a little about ultrasonic electronics modules
- issues in quantitative ultrasonic imaging
- tactile sensors & displays
  - (if not covered in a future student lecture)

---
the jargon of sound measurement
the jargon of
sound measurement

---
sound pressure level (SPL)
sound pressure level (SPL)
- “threshold of audibility”, the minimum pressure fluctuation detected by the ear, is less than 10-9 of atmospheric pressure or about 2 x 10-5 n/m2 at 1000 Hz
- “threshold of pain”: pressure 105 times greater
  (still less than 1/1000 of atmospheric pressure)
- because of the wide range, sound pressure measurements are made on a logarithmic (decibel) scale
- “sound pressure level” (SPL) = 20 log(P/P0) =
  10 log(P/P0)2, where P0= 2 x 10-5 newton/meter2
  - because energy and power scale as pressure squared
  - caution: pay attention to when P = pressure and when P = power
SPL is proportional to the average squared amplitude

---
sound power (SP & PWL)
sound power (SP & PWL)
- SP = total sound power W emitted by a source in all directions
  (in watts = joules/second)
- sound power level
  PWL = 10 log(W/W0) decibels
  - where W0 = 10-12 watt (by definition)
= 10 log(P/P0)2 decibels
        = 20 log(P/P0) decibels
in terms of pressure

---
sound intensity level (IL)
sound intensity level (IL)
- rate of energy flow across unit area
- sound intensity level
  IL = 10 log(I/I0)
  - where I0 = 10-12 watt/meter2

---
multiple sources
multiple sources
two equal sources produce a 3 dB increase in sound power level
  - because log102 = 0.301029996
            10 log102 ≈ 3
- two equal sources produce a 3 dB increase in sound pressure level (assuming on average no interference,
  i.e., incoherent random phases)
- for example, when two 80 dB SPL sources add
  the result is an 83 dB SPL
  (assuming they are incoherent)

---
tying all these & more together …
tying all these & more together …
see http://en.wikipedia.org/wiki/Sound_energy_density

---
exercise
An acoustic sensor, in the absence of any signal of interest, outputs an RMS noise level of 500 μV. When an acoustic signal of interest is added, the sensor’s RMS output becomes 1300 μV. What is the signal-to-noise power ratio expressed in decibels? What would it be if the sensor’s RMS output were to become 2 V when signal of interest is added? [Note: be careful about (1) how RMS quantities add (2) the distinction between signal-to-noise and (signal+noise)-to-noise]

---
ranging by wave packet ToF
ranging by wave packet ToF
- emit a pulse of acoustic energy
- detect its echoes from nearby objects
- measure the time-of-flight (ToF) of each
- multiply by speed-of-sound to get ranges
- issues:
  - directionality: which object at which azimuth
  - signal diminishes with range
    - spreading: energy density decrease (1/z2)
      - all waves diminish as 1/z(dimensionality_of_space -1)
    - attenuation: energy loss to heat (exponential)
      - inherent in nature of sound (but not light)

---
the “wave packet” concept
the “wave packet” concept
a “wave packet” is a finite-duration burst
of transmitted energy (acoustic, light, etc)
  - τ measures its duration
  - to measures its mean time
  - often it is – or is approximated as – Gaussian:
    A(t) = Ao exp[-((t-to)/τ)2] cos(2π f (t-to))

---
problem: range jumps
problem: range jumps
cheap systems commonly detect the time
of echo amplitude crossing a threshold
threshold ~ 0.2
threshold ~ 0.1

---
solution: matched filter
solution: matched filter
- correlate incoming signal with its expected shape, i.e., the shape of the outgoing pulse
- but it’s not quite as easy as you would like:
  dispersion and differential attenuation
  distort the echo vs. the outgoing pulse
  - dispersion: velocity depends of frequency
    - issue for sound and for light in a medium
  - differential attenuation: amplitude decay per unit distance covered depends on frequency
    - this is the energy dissipation phenomena,
      not the universal geometrical spreading

---
nevertheless, here is a seat-of-the-pants picture of how matched filters work
nevertheless,
here is a seat-of-the-pants
picture of how
matched filters work

---
envelopes of pulse and echo
envelopes of pulse and echo

---
underlying ultrasonic oscillation
underlying ultrasonic oscillation

---
pulse – guess – echo
pulse – guess – echo

---
guess * echo when error = 0. period
guess * echo when error = 0. period

---
guess * echo when error = .25 period
guess * echo when error = .25 period

---
guess * echo when error = .5 period
guess * echo when error = .5 period

---
guess * echo when error = .75 period
guess * echo when error = .75 period

---
guess * echo when error = 1.0 period
guess * echo when error = 1.0 period

---
integral of guess * echo over time plotted as function of guess
integral of guess * echo over time
plotted as function of guess

---
exercise
Describe the frequency spectrum of the wave packet used in the previous example.
[hint: In general Δf Δt ≥ 1/(4π), and for a Gaussian envelope ≥ can be replaced by ≈.
A wave packet that is Gaussian in time has a Gaussian frequency spectrum. Given all that, you need only to estimate its center & width.]
How will dispersion and differential attenuation affect time-of-flight measured by this method?

---
problem: beam width
problem: beam width
specular surfaces are visible – by specular reflection – at “non-specular” angles
walls appear as arcs in ultrasonic range images
(that use co-located transmitter and receiver)

---
so walls appear as broken arcs:
(when using threshold detection)

---
since as the signal gets weaker (with angle) the apparent time-of-flight gets longer ...

---
survey of transducers and electronic modules for ultrasonic range sensing
survey of
transducers
and
electronic modules
for
ultrasonic range sensing

---
Polaroid (electrostatic) transducers
Polaroid (electrostatic) transducers
http://www.robotstorehk.com/sensor/sensor.html
http://www.robotstore.com/download/3-740_Sonar_Exp_instr_1.02.pdf

---
Polaroid-transducer systems
Polaroid-transducer systems

---
Polaroid-transducer instruments
Polaroid-transducer instruments
http://www.calculated.com/UsersGuides/3302mn.pdf

---
Panasonic (piezoelectric)  transmitters and receivers
Panasonic (piezoelectric)
transmitters and receivers

---
beam “width” (angular distribution)

---
sensitivity vs. frequency & load
sensitivity vs. frequency & load

---
frequency & output vs. drive
frequency & output vs. drive

---
received signal vs. distance
received signal vs. distance

---
Massa 40 kHz & 75 kHz Models
Massa 40 kHz & 75 kHz Models

---
impedance & angular distribution
impedance & angular distribution
Note higher frequency
 (shorter wavelength)
     has narrower beam

---
the “strange” resonance characteristics of piezo-electric transducers
the “strange”
resonance characteristics
of
piezo-electric transducers

---
resonance characteristics
resonance characteristics

---
impedance vs. frequency
impedance vs. frequency

---
sonar electronics modules
sonar electronics modules

---
time-dependent amplification
time-dependent amplification
- receiver amplifier gain is typically “ramped” approximately linearly with
  time after acoustic pulse emission
- this helps suppress direct coupling (i.e., not via echo) between transmitted pulse and electronic detection circuit
- but primarily it is used to compensate signal strength fall off with distance
- but you can’t do it forever … eventually you’ll just be amplifying noise

---
circuit layout issues to achieve isolation of transmit and receive
circuit layout issues to achieve isolation of transmit and receive

---
IC for sonar applications
IC for sonar applications

---
circuit functional details
circuit functional details

---
TI TL851/2 hybrid analog-digital
TI TL851/2 hybrid analog-digital
often used with Polaroid (electrostatic) transducers as alternative to the
Polaroid-supplied electronics

---
some issues in
quantitative
ultrasonic
imaging

---
e.g., in medical imaging …
e.g., in medical imaging …
speed of sound in “flesh and blood” is:
  - not known
  - not constant (even in one individual subject)
  - not amenable to measurement using “manufactured artifacts”
so if precisely scaled range is needed,
an “in situ” calibration method is required

---
“average” or “typical” values are fine:
  - for qualitative visualization,
    pathology / diagnosis, etc
  - but probably not for, e.g.,
    custom design of wheelchair cushions
  - and certainly not for, e.g.,
    planning a micro-surgical path

---
problem
problem
image guided surgery literature seeks:
  - navigational accuracy ~ 1 mm
  - endpoint precision ~ 0.1 mm
ignorance of precise acoustic properties of skin, fat, muscle, etc, layers makes these specifications problematic

---
approach
approach
- identify elementary cases
- invent in situ calibration protocols for them:
  - multiple parallel homogeneous layers
  - speed of sound gradient in a single layer
  - a tapered layer
assume
  - any real case is a (separable) combination
    of the elementary cases
  - mechanically accurate scanning capability

---
basic ToF technique
basic ToF technique
a single-sided ultrasonic thickness measurement method
  - presumes speed of sound ci is known

---
and a differential method
  - presumes speed of sound ci does not change with thickness

---
one homogeneous layer
one homogeneous layer
two (or more) oblique paths
  - overcomes the presumptions of the
    normal path methods
  - however, possible confusion from
    diffuse reflection!
  - if i>2 a least-squares solution will
    optimize accuracy

---
several parallel  homogeneous layers
several parallel
homogeneous layers
select two values of x1; measure corresponding two values of x2
  - mainstay of geoacoustics, e.g.,
    oil prospecting in complex rock strata
  - need to assume the paths are distinguishable by, e.g., signal amplitude

---
parallel layers with velocity gradient
parallel layers with velocity gradient
sinc = k holds even if c is a function of position
  - acoustic trajectory is then curved)
- continuous c causes refraction but not reflection
- if c is a linear function of position (depth)
  then the curved path is a circular arc
- this result is a mainstay of underwater acoustics, where temperature and salinity gradients lead to speed-of-sound gradients
- three T/R separations are enough to measure
  c0, z, and the launch angles {1, 2, 3} corresponding to the chosen {x1, x2, x3}

---
note: compare with the
“mirage” effect, where
you have reflection
that doesn’t require any
reflecting surface

---
nonparallel layers
nonparallel layers
- acoustic time-of-flight defines an elliptical locus to which the reflecting discontinuity is tangent
- there is usually only one physically reasonable line that is tangent to two such ellipses
  - so if c is known, two {xi,ti} pairs fix the depth
    and angle of inclination of the reflecting plane
  - an additional pair will resolve any ambiguity
  - when c is not known in advance, an additional pair is sufficient to find both c and the correct reflecting plane

---
tactile sensors
&
displays

---
recommended reading
recommended reading
classic tactile sensing articles for history:
  - Nicholls & Lee (~1990)
  - Leon Harmon (~1982)
- current robotics literature for latest gadgets
- articles cited
  - older articles on next page
  - hopefully newer articles cited in
    up-coming student lecture

---
older tactile sensing literature
older tactile sensing literature
- Harmon, L.D., Automated Tactile Sensing. International Journal of Robotics Research, 1982. 1(2): p. 3-32.
- Pugh, A., Tactile and Non-Vision. Robot Sensors, ed. A. Pugh. Vol. 2. 1986, Bedford UK: IFS (Publications) Ltd and Springer-Verlag.
- Nicholls, H.R. and M.H. Lee, A Survey of Robot Tactile Sensing Technology. International Journal of Robotics Research, 1989. 8(3): p. 3-30.
- Ron Fearing: http://robotics.eecs.berkeley.edu/~ronf/tactile.html
- National Academy Press, Expanding the Vision of Sensor Materials. 1995. (Appendix A, references)
  http://books.nap.edu/books/0309051754/ 101.html#pagetop
- also: medical-tactile sensing (not covered explicitly here)

---
tactile sensing
tactile sensing
simulating (sensors)
and
stimulating (displays)
the
human sense of touch

---
human skin tactile sensitivity
human skin tactile sensitivity
- at least four different kinds of sensor cells
- different spatial and frequency sensitivities

---
speculative specifications fingers
speculative specifications fingers
- “ideal stimulator” would provide 50 N/cm2 peak pressure, 4 mm stroke, and 25 Hz BW (Fearing)
- skin acts like a spatial low-pass filter
  - when we handle flexible materials (fabric, paper) we sense the pressure variation across the finger tip
- fingertip mechanoreceptor bandwidth ~30 Hz
- density 70 cm-2 (resolve ~1.2 mm between points)
- finger curvature, thermal properties, and other environmental factors seem critical to teletaction

---
conceptual tactile sensor array (Fearing)
conceptual tactile sensor array (Fearing)
and mine ~1983

---
current haptic interfaces and tactile displays
and mine ~1985
virtual reality
people with disabilities
UC Berkeley
Robotics Lab
John Hopkins University
Somatosensory Labs
MIT’s Phantom (now by startup SenSation)

---
tactile sensor requirements
tactile sensor requirements
see the Leon Harmon articles:
  - surveyed industry, government, research people to ascertain the specs they thought tactile sensing for robotic assembly etc. required
  - (but how did they know??)
“blue sky” and practical requirements:
  - skin-like sensors, hand-like actuators, low-level processing
  - practical specifications summarized in Nicholls article
financed by Lord Corporation
  - defunct product: tactile sensor array for robotics

---
a solution in search of a problem?
a solution in search of a problem?
- identification or location?
- agree with Nicholls and Lee’s conclusion that vision is well-developed and probably fundamentally better for identification ... better role for tactile is precise relative location
- difficulty & importance of slip sensing
  - literature often mentions “incipient slip”, but it is never clear what it means
  - coefficient of friction decreases once slip begins, making recovery difficult

---
real-world applications of tactile sensing
real-world applications of tactile sensing
T. Goto, T. Inoyama, K. Takeyasu (Hitachi, Japan): Precise Insert Operation by Tactile-Controlled Robot (in the Pugh book, 1986!!)
  - “The HI-T-HAND Expert-1 assembly robot has now been completed. Its delicate tactile control is capable of inserting a shaft into a hole with a clearance of 20 micrometers, faster and more dexterously than in a human operation. It is impossible for conventional robots and automatic assembling machines to perform such operations of precision insertion. Accordingly, such operations have been left for man’s hand to perform. Now, however, the sequence controller makes it possible, without the use of a computer for robots to perform certain of these functions.”
this is the ONLY one I know!

---
technologies  for tactile sensing
technologies
for tactile sensing

---
you name it, IT’S BEEN TRIED!
you name it, IT’S BEEN TRIED!
- momentary switch contact
- spring + LVDT or some such analog pressure measurement
  - including MEMS techniques, e.g., strain gauges on diaphragms
- force sensitive resistor (with or without built-in mechanical threshold)
- capacitative or optical measurements of surface deformation
- liquid crystal (color &/or opacity changes with deformation)

---
- total internal reflection
  (e.g., for fingerprints)
- phonograph needle for slip/vibration
  (do you know what it is?)
- thermistors etc for temperature/thermal conductivity etc
- piezoelectric, pyroelectric (e.g., PVDF)
- etc etc etc

---
- most commonplace, maybe most promising: “touch pad” capacitive arrays
  http://www.synaptics.com/technology/cps.cfm
- exception to the generalization:
  this is a “proximity” vs. a “pressure” sensor!
a good example of the
principle that if Y (in
the environment) makes
X (a resistor, capacitor,
etc) BAD, then a BAD
design for X can be
exploited to as a
GOOD sensor for Y

---
a little philosophy: the synergy of sensor & display development
a little philosophy:
the synergy of
sensor & display
development

---
tactile displays THEN tactile sensors?
tactile displays THEN tactile sensors?
television and telephone: analogy
  - contrived sensor is secondary to natural display
    - make the best speaker you can ... then optimize microphone
    - make the best TV display you can ... then optimize camera
    - (until recently ... computer-understanding changes the rules ...)
radar and sonar: contrast
  - contrived display is secondary to a trans-human sensor
    - raw data initially as peaks, wiggles, etc, in signal vs. time plot
    - human-centered displays later conceived and developed for non-experts, natural interpretation even by experts, etc

---
a principle?
a principle?
there is no point in making a display with more resolution than your best sensor
  - in any domain:
    spatial, temporal, dynamic range, color, etc
  - (unless you have a virtual sensor that is better!)
there is no point in making a sensor with more resolution than your best display
  - (though in many domains you can “zoom in”)
so improvement cycles display ↔ sensor

---
piezo-resistive sensors
piezo-resistive sensors

---
pressure sensitive resistors (PSR)
pressure sensitive resistors (PSR)
bulk resistance vs. contact resistance

---
PSR magnitude
PSR magnitude
- Nicholls and Lee say few hundred to few thousand ohms is typical ...
- my experience is that common conductive foams (IC packaging etc) etc are typically 1000 - 10000 times higher ...
  - so high impedance measurement techniques must be employed
  - and time response ( = RC) can suffer

---
PSR noise
PSR noise
- no general theory (that I know)
- contact-resistance-based designs are noisy
- surface effects are noisier than volume effects
  - density of opportunities for trouble is higher
    in a space of lower dimensionality
    - a single defect is fatal in 1-dimension
but depending on details of the particular design, under microscopic examination distinction may not be clear
  - bulk resistance change may be due to distortion (A/l)
  - but it can also be due to changes in inter-grain contact

---
exercise
exercise
A cylindrical resistive element is compressed or stretched in a way that does not change its basically-cylindrical shape, and does not change its volume; assuming its resistivity does not change either, derive how ΔR/R (fractional change in resistance) depends on ΔL/L (fractional change in length).

---
piezo-electric sensors
piezo-electric sensors

---
piezo- and pyroelectric devices
piezo- and pyroelectric devices
- piezo- (pressure) and pyro- (heat) electricity are
  always coupled
- it is due to separation of electrical charges in the
  material’s crystalline arrangement
  - electric dipoles at the molecular level (e.g., H2O)
  - high voltage poling to macroscopically align dipoles
  - “electrets” made by poling various waxy mixtures
- pressure  voltage (sensor)
  voltage  deformation (actuator)
- due to leakage, effect is transient
  - to stabilize, leakage is intentionally increased, making device response effectively to dP/dt
high voltage + high input impedance  tiny current
(hard to measure, slow to measure)
O
H
H

---
practical piezoelectric materials
practical piezoelectric materials
quartz (cut along particular crystal axes to maximize piezo- and minimize pyro- effects)
  - effect small but very stable
various ceramics, e.g., ZnO, PZT(TM)
  - deposition on micro- and mini- fabricated devices
    - SAW (surface acoustic wave) devices for sure
    - MEMS devices discussed but not sure whether implemented
plastics: polyvinylidene difluoride (PDVF, PVF2)
  - enormous quantities are reportedly used in submarine sonar transducers
    - yeah, so why is it so expensive?

---
magnitude of piezoelectric effect
magnitude of piezoelectric effect
- easy to get tens of volts but need high input impedance measuring instrument
- can get very high voltages (enough to spark across ~ 1 mm) in response to impact
  - buy yourself a “flintless” butane lighter

---
capacitive sensing
capacitive sensing

---
capacitive devices
capacitive devices
- “mouse pad” or “touch pad” is now ubiquitous, reliable, stable
- same geometrical factors as resistive sensors (but remember that capacitance is defined “upside down”:
  V = L dI/dt + R I + Q/C
- actual approach is to measure distortion in “stray” capacitance
- (again) see http://www.synaptics.com/technology/cps.cfm
- many geometries, including some “finger-like” curvatures

---
magnitude of capacitive effects
magnitude of capacitive effects
0 = 410-7 henry/m, 0 = 0/c2 = 8.85 10-12 farad/m
- “small capacitor” is ~ 100 pF (p = pico = 10-12)
- say you want to see a 1% change in capacitance
- say tactel is 1 mm2, dielectric constant is 10
- then to get 100 pF need l = 10 0 A / C = 10-6 m or 10-3 mm
- and to resolve a 1% change need to see 10-8 m
  - wavelength of green light is around 50 x 10-8 m
- might use multi-layer tricks to improve this
- but the smallness of this effect probably explains why the commercial technology exploits the “stray capacitance” effect vs. pressure-induced capacitance change
  - however: the best vacuum/gas pressure sensors are capacitive

---
miscellaneous tactile sensing schemes
miscellaneous
tactile sensing schemes

---
magnetic and inductive effects
magnetic and inductive effects
- many prototypes, probably no products
- inductive devices are more-or-less miniature LVDTs
- magnetic effects, e.g., magneto-resistance plausible
  - recent developments of “giant” and “colossal” magneto-resistance
    materials may hold promise, but no developments as yet ...
- slip sensing potential with dipoles oriented within surface
- Hall effect sensors may be the most plausible, as Hall effect switches are in common use in computer keyboards etc
Hall effect:
voltage due
to deflection
of current’s
charge carriers

---
deformation of elastomers
deformation of elastomers
many mechanical, optical, and acoustic readout schemes prototyped ...
  - optical? for example, modified total internal reflection schemes (as mentioned above)
  - acoustic? Grahn @ Utah: ultrasonic measurement of compression
typically cumbersome ... probably obsolete except as source of ideas for future MEMS implementations ...

---
fiber optic schemes, e.g.,
Schoenwald @ Rockwell
  - seemed promising
  - potentially “fabric”- or even “skin”-like
  - but never went anywhere commercially
mws@cmu.edu 16722 20080325 L09Ta
sound & tactile

---
miscellaneous issues
miscellaneous issues

---
“finger-like”surfaces
“finger-like”surfaces
- for surfaces with “true gaussian curvature”, little that seems ready for prime-time ...
- R. Fearing, Int. J. Robotics Research, V. 9 #3, June 1990, p.3-23: Tactile Sensing Mechanisms (from his PhD thesis): “fingertip” (cylinder with hemispherical cap), with capacitive pressure sensor embedded in the cylindrical (only) part
  - 8 circumferential x 8 axial electrode array in molded rubber
  - capacitance measured at 100 kHz; scanned at 7 Hz
  - maybe cylindrical surfaces are not so bad
    - e.g., it is useful to be able to bend planar sheets
  - problems with hysteresis and creep, coupling between tactels, modelling response to fingertip loading
  - paper is good example of a complete electrical/mechanical model

---
related area: proximity sensing
related area: proximity sensing
- frustrated by lack of good “touch sensors”, there have been several (mostly Japanese) demonstrations of object identification by scanning a short range (~1 cm) “robot fingertip” proximity sensor.
- four competitive moderate-cost commercial technologies:
  - capacitive best for dielectric (insulating) materials
  - inductive best for metallic (conducting) materials
  - optical: simple transmitter-receiver pair, e.g., Radio Shack
  - acoustic: probably for somewhat longer range
some proven but less developed and accepted ways:
  - fiber optic bundles
  - focus based methods (e.g., using CD-player components)
  - (field emission/tunneling/discharge/ etc. are a bit far out)
    - sensitive but difficult to calibrate

---
MEMS tactile display development (mostly CMU)
MEMS tactile display development (mostly CMU)
thanks to George Lopez

---
MEMS actuators for tactile stimulation
 - two sealed chambers sharing common membrane
 - inner chamber out-of-plane force/deflection caused by
  electrostatic compression of outer chamber
 - move towards integrated actuator and control, all “on-chip”;
  experiment now with CMOS membranes
Tactile displays in “on” position
Si substrate
Polymer seal
Metal 1 + Oxide Layer
Metal 2 + Oxide Layer
+
-

---
MEMS tactile stimulator array concept
An individual
MEMS-based
taxel (tactile pixel)
stimulator off
(no applied
voltage)
cross-sectional
view
common membrane
stimulator on
(applied voltage
creates electrostatic
deflection)
concentric chambers
with shared, sealed volumes
A 10 x 10
tactile stimulator array
1 cm
1 cm

---
test taxel chip fabrication results
tactile stimulator test chip
with 11 different inner
radii
openings between inner
and outer chamber volume
50 m
bottom electrode of
actuator (polysilicon)
Kapton common
membrane (post-fab)
Linner
1.54 mm
Louter
upper electrode of
actuator (polysilicon)

---
long term goal: build on flexible silicon membranes