Atomic orbital considerations in metal chemistry

The solution to the Schrödinger equation, a bound electron in a central force environment, only has solutions for a two body system i.e. the hydrogen atom, assuming that the nucleus is structureless and acts as a point charge. These analytic solutions are termed hydrogenic solutions or hydrogenic orbitals for obvious reasons, though in principle, the same calculation can be performed for "U"^{91 {}+{}} .
Although Cartesian coordinates are often the most intuitive to use, having well-understood relationships with a simple volume element d V=dx dy dz and so on, the formulation of the Schrödinger equation in Cartesians viz

-{hbar ^{2}} over {2 m} left ( {partial^{2}} over {partial {x}}+{partial^{2}} over {partial {y}}+{partial^{2}} over {partial {z}} + {hat {V}(x,y,z)} right ) %PSI_{n} (x,y,z)=E_{n} %PSI_{n} (x,y,z)

is insoluble as the variables are not separable.
A coordinate change to spherical polar coordinates

(x,y,z)rightarrow(r,%varphi,%theta)

presents us with a complicated but soluble equation, in which the variables are fully separable. The kinetic energy portion of the Hamiltonian {hat {T}}_{K} is then written as

{hat {T}}_{K}=-{hbar ^{2}} over {2 m} left ( {{1} over {r}}{partial^{2} {}} over {partial r^{2}}+{{1} over {r^{2} sin^{2} %phi}}{partial^{2} {}} over {partial %phi^{2}}+{{1} over {r^{2} sin %phi}}{partial {}} over {partial %phi} sin %phi {partial {}} over {partial %phi} right )

and the potential, {hat {V}} , is written as

{hat {V}}={hat {V}}_{Coul}+{hat {V}}_{rot}=-{{Z e^{2}} over {4 %pi %varepsilon_{0} r}}+{{l(l+1) hbar^{2}} over {2 %mu r} }

which leads to solutions that are of the form

%PSI_{n,l,m_{l}} (r,%theta,%phi)=R(r)Y(%theta,%phi)

i.e. an angular wavefunction and a radial wavefunction.
The angular functions are also the wavefunctions associated with angular momentum and they therefore behave as such, giving rise to angular orbital momentum, denoted by the quantum number l with a direction denoted by the quantum number m_{l} . These functions provide the angular shapes of the orbitals, determine the angular nodal properties and also the symmetrical properties associated with crystal and ligand field calculations.
The radial functions primarily determine the crude energies of the orbitals and the nodal properties of these functions determine the trends down the various groups in terms of qualitative concepts such as shielding and penetration, which have profound effects on the chemistries of the various elements.
The solutions of the Schrödinger equation are complicated and involve recursion relations that depend on the quantum numbers; derivations of the general solutions can be found in most quantum mechanics textbooks, such as Messiah, and will not be presented here. The wavefunctions, which contain two types of Special Functions, are given by

%psi_{n l m_{l}}(%theta,%phi,r) = sqrt {{left ({alignc 2 Z} over {alignc n a_{%mu}} right ) }^3 {alignc fact (n-l-1)} over {alignc 2 n[fact (n+l)]} } e^{{alignc - Z r } over {alignc n a_{%mu}}} left ({alignc 2 Z r} over {alignc n a_{%mu}} right )^{l} L_{n-l-1}^{2l+1} left ({alignc 2 Z} over {alignc n a_{%mu}} right ) cdot Y_{l,m}(%theta, %phi )

where a_{%mu} = {{4 %pi %varepsilon_0 hbar^2} over{%mu e^2}} , Y_{l,m}(%theta, %phi ) are the spherical harmonics and L_{n-l-1}^{2l+1} are the associated Laguerre polynomials. The importance of these special functions lies not in the details of their mathematical relationships, but rather in the general forms that they take. We will reserve a discussion of the angular functions until we discuss the importance of angular momentum in transition metal chemistry and concentrate here on the radial functions.
Solutions to the Schrödinger equation are in general complex and for any value of l , there is only one real orbital, which has m_{l}=0 when clearly left none e^{i m_{l} %phi} right rline _{m_{l}=0}=1 . It is often easier to visualize real orbitals and these are obtained by taking linear combinations of +- m_{l} pairs within one value of l which will yield orthonormal real pairs of orbitals. Recalling De Moivre's theorem and the Euler representation of a complex number, i.e. e^{i A} = cos A + i sin A , and applying this to say the functions for l = 1 , namely R_{n,1} cdot Y_{-1}^{1} , R_{n,1} cdot Y_{0}^{1} and R_{n,1} cdot Y_{1}^{1} , we obtain,

matrix { alignl {R_{n,1} cdot Y_{-1}^{1}=R_{n,1} cdot sqrt{3 over 4} sin %theta cdot e^{-i %phi}} # p_{-1} ## alignl {R_{n,1} cdot Y_{0}^{1}=R_{n,1} cdot sqrt{3 over 2} cos %theta} # p_{0} ## alignl { R_{n,1} cdot Y_{1}^{1}=R_{n,1} cdot sqrt{3 over 4} sin %theta cdot e^{i %phi}} # p_{1} }

Expanding the exponential term using e^{i A} = cos A + i sin A ,

matrix { alignl {R_{n,1} cdot Y_{-1}^{1}=R_{n,1} cdot sqrt{3 over 4} sin %theta cdot left (cos %phi - i sin %phi right)} # p_{-1} ## alignl {R_{n,1} cdot Y_{0}^{1}=R_{n,1} cdot sqrt{3 over 2} cos %theta} # p_{0} ## alignl { R_{n,1} cdot Y_{1}^{1}=R_{n,1} cdot sqrt{3 over 4} sin %theta cdot left (cos %phi + i sin %phi right)} # p_{1} }

and then taking linear combinations of p_{-1} and p_{1} we have

alignl R_{n,1} cdot Y_{-1}^{1}+R_{n,1} cdot Y_{1}^{1} = R_{n,1} cdot sqrt{3 over 4} sin %theta cdot left (cos %phi - i sin %phi right) + R_{n,1} cdot sqrt{3 over 4} sin %theta cdot left (cos %phi + i sin %phi right) newline alignl R_{n,1} cdot Y_{-1}^{1}+R_{n,1} cdot Y_{1}^{1} = R_{n,1} cdot 2 sqrt{3 over 4} sin %theta cdot cos %phi

given that in spherical polar coordinates, alignl x = r sin %theta cos %phi , then

alignl p_{-1}+ p_{1} = R_{n,1} cdot Y_{-1}^{1}+R_{n,1} cdot Y_{1}^{1} = R_{n,1} cdot 2 sqrt{3 over 4} sin %theta cdot cos %phi = R_{n,1} cdot 2 sqrt{3 over 4} cdot {x over r} prop x ,

which we identify with the p_{x} orbital. Linear combinations of +- m_{l} pairs of any of the left ( 2 l+1 right ) m_{l} orbitals for a given l will yield real wavefunctions, when normalized.

matrix{ "orbital" # %psi_{n l m_{l}}(r, %theta,%phi) # %psi^{real}_{n l m_{l}}(r, %theta,%phi) ## {} # {} # {} ## 1 s # {{alignc 1} over {sqrt {%pi} a_{0}^{3/2}}} cdot e^{-r over a_{0}} # left (1 over sqrt %pi right ) left (Z over a right )^{3 over 2} e^{-Zr over a} }

matrix{ "orbital" # alignl ~~~~~~ %psi_{n l m_{l}}(r, %theta,%phi) # alignl ~~~~~~%psi^{real}_{n l m_{l}}(r, %theta,%phi) ## {} # {} # {} ## 2 s # alignl {{alignc 1} over {4 sqrt {2 %pi} a_{0}^{3/2}}} cdot left (2-{r} over {a_{0}} right ) cdot e^{-r over {2 a_{0}}} # alignl left (1 over sqrt {32 %pi} right ) left (Z over {alignc a} right )^{3 over 2} left (2 - Zr over {alignc a} right) e^{-Zr over{alignc 2 a}} ## {} # {} # {} ## 2 p # alignl {{alignc 1} over {4 sqrt {2 %pi} a_{0}^{3/2}}} cdot {{r} over {a_{0}}} cdot e^{-r over {2 a_{0}}} cdot cos %theta # alignl left (1 over sqrt left (32 %pi right ) right ) left (Z over {alignc a} right )^{5 over 2} r e^{-Zr over {alignc 2 a}} cos %theta ## 2 p # {{alignc 1} over {8 sqrt { %pi} a_{0}^{3/2}}} cdot {{r} over {a_{0}}} cdot e^{-r over {2 a_{0}}} cdot sin %theta cdot e^{+- i %phi} # left lbrace {matrix { left (1 over sqrt left (32 %pi right ) right ) left (Z over {alignc a} right )^{5 over 2} r e^{-Zr over {alignc 2 a}} sin %theta sin %phi ## left (1 over sqrt left (32 %pi right ) right ) left (Z over {alignc a} right )^{5 over 2} r e^{-Zr over {alignc 2 a}} sin %theta cos %phi }} right none }

matrix{ "orbital" # alignl ~~~~~~~~~ %psi_{n l m_{l}}(r, %theta,%phi) # alignl ~~~~~~~~~ %psi^{real}_{n l m_{l}}(r, %theta,%phi) ## {} # {} # {} ## 3 s # alignl {{alignc 1} over {81 sqrt {3 %pi} a_{0}^{3/2}}} cdot {left (27 - 18 {r} over {a_{0}} + 2 {r^2} over {a_{0}^2} right )} cdot e^{-r over {3 a_{0}}} # 1 over left (81 sqrt left (3 %pi right ) right ) left (Z over {alignc a} right )^{3 over 2} left (27 - 18 Zr over {alignc a} + 2 left (Zr over {alignc a} right )^{2} right ) e^{-Zr over {alignc 3 a}} ## {} # {} # {} ## 3 p # alignl {{alignc {sqrt 2}} over {81 sqrt {%pi} a_{0}^{3/2}}} cdot left ({6 - {r} over {a_{0}}} right ) cdot { {r} over {a_{0}} } cdot e^{-r over {3 a_{0}}} cdot cos %theta # alignl left ( sqrt 2 over 81 sqrt %pi right ) left (Z over {alignc a} right )^{5 over 2} left (6 - Zr over {alignc a} right ) r e^{-Zr over {alignc 3 a}} cos %theta ## 3 p # {{alignc {sqrt 2}} over {81 sqrt {%pi} a_{0}^{3/2}}} cdot left ({6 - {r} over {a_{0}}} right ) cdot { {r} over {a_{0}} } cdot e^{-r over {3 a_{0}}} cdot sin %theta cdot e^{+- i %phi} # alignl left lbrace {matrix { left ( sqrt 2 over 81 sqrt %pi right ) left (Z over {alignc a} right )^{5 over 2} left (6 - Zr over {alignc a} right ) r e^{-Zr over {alignc 3 a}} sin %theta sin %phi ## left ( sqrt 2 over 81 sqrt %pi right ) left (Z over {alignc a} right )^{5 over 2} left (6 - Zr over {alignc a} right ) r e^{-Zr over {alignc 3 a}} sin %theta cos %phi }} right none ## {} # {} # {} ## 3 d # alignl {{alignc {1}} over {81 sqrt {6 %pi} a_{0}^{3/2}}} cdot {{r^{2}} over {a_{0}^{2}}} cdot e^{-r over {3 a_{0}}} cdot left (3 cos^{2} %theta -1 right ) # alignl left (1 over 81 sqrt left (6 %pi right ) right ) left (Z over {alignc a} right )^{7 over 2} r^{2} e^{-Zr over {alignc 3 a}} left (3 cos^{2} %theta - 1 right ) ## 3 d # alignl {{alignc {1}} over {81 sqrt {%pi} a_{0}^{3/2}}} cdot {{r^{2}} over {a_{0}^{2}}} cdot e^{-r over {3 a_{0}}} cdot left (sin %theta cos %theta right ) cdot e^{+- i %phi}#alignl left lbrace {matrix { left ( sqrt 2 over 81 sqrt %pi right ) left (Z over {alignc {alignc a}} right )^{7 over 2} r^{2} e^{-Zr over {alignc 3 a}} sin %theta cos %theta sin %phi ## left ( sqrt 2 over 81 sqrt %pi right ) left (Z over {alignc a} right )^{7 over 2} r^{2} e^{-Zr over {alignc 3 a}} sin %theta cos %theta cos %phi }} right none ## 3 d # alignl {{alignc {1}} over {162 sqrt {%pi} a_{0}^{3/2}}} cdot {{r^{2}} over {a_{0}^{2}}} cdot e^{-r over {3 a_{0}}} cdot left (sin^{2} %theta right ) cdot e^{+- 2 i %phi} # alignl left lbrace {matrix { left (1 over 81 sqrt left (2 %pi right ) right ) left (Z over {alignc a} right )^{7 over 2} r^{2} e^{-Zr over {alignc 3 a}} sin ^{2} %theta sin left (2 %phi right ) ## left (1 over 81 sqrt left (2 %pi right ) right ) left (Z over {alignc a} right )^{7 over 2} r^{2} e^{-Zr over {alignc 3 a}} sin ^{2} %theta cos left (2 %phi right ) }} right none }

matrix{ "orbital" # alignl ~~~~~~~~~~~~~~~~~~~~~ %psi^{real}_{n l m_{l}}(r, %theta,%phi) ## {} # {} ## 4 s # alignl left ({alignc 1} over 1536 sqrt %pi right ) left (Z over {alignc a} right )^{3 over 2} left (192 - 144 left (Zr over {alignc a} right ) + 24 left (Zr over {alignc a} right )^{2} - left (Zr over {alignc a} right )^{3} right ) e^{-Zr over {alignc 4 a}} ## {} # {} ## 4 p_{y} # alignl left ({alignc 1} over 512 sqrt left (5 %pi right ) right ) left (Z over {alignc a} right )^{5 over 2} left (80 - 20 left (Zr over {alignc a} right ) + left (Zr over {alignc a} right )^{2} right ) r e^{-Zr over {alignc 4 a}} sin %theta sin %phi ## 4 p_{z} # alignl left ({alignc 1} over 512 sqrt left (5 %pi right ) right ) left (Z over a right )^{5 over 2} left (80 - 20 left (Zr over a right ) + left (Zr over a right )^{2} right ) r e^{-Zr over {alignc 4 a}} cos %theta ## 4 p_{x} # left (1 over 512 sqrt left (5 %pi right ) right ) left (Z over a right )^{5 over 2} left (80 - 20 left (Zr over a right ) + left (Zr over a right )2 right ) r e^{-Zr over {alignc 4 a}} sin %theta cos %phi ## {} # {} ## 4 d_{xy} # alignl left ( {alignc sqrt 3} over 1536 sqrt %pi right ) left (Z over {alignc a} right )^{7 over 2} left (12 - Zr over {alignc a} right ) r^{2} e^{-Zr over {alignc 4 a}} sin ^{2} %theta sin left (2 %phi right ) ## 4 d_{yz} # alignl left ( {alignc sqrt 3} over 3072 sqrt %pi right ) left (Z over {alignc a} right )^{7 over 2} left (12 - Zr over {alignc a} right ) r^{2} e^{-Zr over {alignc 4 a}} sin %theta cos %theta sin %phi ## 4 d_{z^{2}} # alignl left ({alignc 1} over 3072 sqrt %pi right ) left (Z over {alignc a} right )^{7 over 2} left (12 - Zr over {alignc a} right ) r^{2} e^{-Zr over {alignc 4 a}} left (3cos^{2} %theta - 1 right ) ## 4 d_{xz} # alignl left ( {alignc sqrt 3} over 3072 sqrt %pi right ) left (Z over {alignc a} right )^{7 over 2} left (12 - Zr over {alignc a} right ) r^{2} e^{-Zr over {alignc 4 a}} sin %theta cos %theta cos %phi ## 4 d_{x^{2}-y^{2}} # alignl left ( {alignc sqrt 3} over 1536 sqrt %pi right ) left (Z over {alignc a} right )^{7 over 2} left (12 - Zr over {alignc a} right ) r^{2} e^{-Zr over {alignc 4 a}} sin ^{2} %theta cos left (2 %phi right ) ## {} # {} ## 4 f_{y left (3x^{2}-y^{2}right )} # alignl left ({alignc 1} over 3072 sqrt left (2 %pi right ) right ) left (Z over {alignc a} right )^{9 over 2} r^{3} e^{-Zr over {alignc 4 a}} sin ^{3} %theta sin left (3 %phi right ) ## 4 f_{xyz} # alignl left ( {alignc sqrt 3} over 3072 sqrt left (2 %pi right ) right ) left (Z over {alignc a} right )^{9 over 2} r^{3} e^{-Zr over {alignc 4 a}} sin 2 %theta cos %theta sin left (2 %phi right ) ## 4 f_{yz^{2}} # alignl left ( {alignc sqrt 3} over 3072 sqrt left (10 %pi right ) right ) left (Z over {alignc a} right )^{9 over 2} r^{3} e^{-Zr over {alignc 4 a}} sin %theta left (5 cos^{2} %theta - 1 right ) sin %phi ## 4 f_{z^{3} } # alignl left ({alignc 1} over 3072 sqrt left (5 %pi right ) right ) left (Z over {alignc a} right )^{9 over 2} r^{3} e^{-Zr over {alignc 4 a}} left (5 cos^{3} %theta - 3cos %theta right ) ## 4 f_{xz^{2} } # alignl left ( {alignc sqrt 3} over 3072 sqrt left (10 %pi right ) right ) left (Z over {alignc a} right )^{9 over 2} r^{3} e^{-Zr over {alignc 4 a}} sin %theta left (5cos^{2} %theta - 1 right ) cos %phi ## 4 f_{z left (x^{2}-y^{2} right )} # alignl left ( {alignc sqrt 3} over 3072 sqrt left (2 %pi right ) right ) left (Z over a right )^{9 over 2} r^{3} e^{-Zr over {alignc 4 a}} sin ^{2} %theta cos %theta cos left (2 %phi right ) ## 4 f_{x left (x^{2}-3y^{2} right )} # alignl left ({alignc 1} over 3072 sqrt left (2 %pi right ) right ) left (Z over {alignc a} right )^{9 over 2} r^{3} e^{-Zr over {alignc 4 a}} sin ^{3} %theta cos left (3 %phi right ) }