## Slide 1
May 10, 2022 | MC TELECONFERNCE
Doug Smith
Technical manager
Proposed change to expand options for storage resources to utilize the CSF model
Improve Continuous Storage Facility (CSF) Model

## Slide 2
CSF Model Improvement
WMPP ID:
165
Proposed Effective Date: November 1, 2022
The ISO proposes to improve the CSF model to accommodate storage resources that inject energy into the grid, but do not consume energy from the grid
  These new storage resource configurations emerged after the CSF rules were originally developed
  The current Tariff rules do not allow these resources to use CSF model
The goal of this project is to allow storage resources with an inject-only configuration the option of participating as a CSF
This is the first Markets Committee Meeting
  This presentation introduces the problem and proposed solution

## Slide 3: Problem Statement
The CSF rules currently limit participation to resources that are capable of consuming energy from and injecting energy into the ISO administered bulk electric system (BES)
Some new resource configurations consisting of storage plus intermittent generation are not capable of consuming energy from the BES because they must charge their storage from the on-site generation

## Slide 4: Proposal
To address the issue, we propose tariff changes to III.1.10.6 that would allow storage resources to register and operate as a CSF even if they cannot consume charging energy from the grid
These tariff changes will allow storage resources in the above-mentioned configuration to use the CSF model to provide all wholesale market services they are capable of providing
In many cases, the CSF model is superior to alternative options for registering an inject-only storage resource
  The CSF model allows the ISO greater visibility and dispatch control
  The CSF model allows the participant comprehensive access to all markets as a single asset

## Slide 5: Summary of Proposed Tariff Changes
Tariff Section | Tariff Change | Reason for Change
III.1.10.6 | A storage facility is a facility that is capable of receiving electricity from the grid and storing the energy for later injection of electricity back into the grid. A storage facility may participate in the New England Markets as described below. | The description of a storage facility in III.1.10.6 is broadened to include facilities that cannot receive electricity from the grid.
III.1.10.6(a)(ii) | (An Electric Storage Facility shall:)… ii. have the ability to inject at least 0.1 MW, and, except for those facilities described in subsection (c) below, and consume at least 0.1 MW; | Allow storage facilities that cannot charge their energy storage from the grid to use the CSF model that is described in III.1.10.6(c)

## Slide 6: Conclusion
The ISO proposes to improve the CSF model by allowing it to be used by storage resources that inject energy into the grid, but do not consume energy from the grid
The proposed effective date is November 1, 2022

## Slide 7: Stakeholder Schedule
Stakeholder Committee and Date | Scheduled Project Milestone
Markets Committee May 10, 2022 | Introduce problem and proposed solution
Markets Committee June 7-8, 2022 | Additional committee discussion
Markets Committee July 12-14, 2022 | Vote
Participants Committee August 4, 2022 | Vote

## Slide 8
Doug Smith
(413) 540-4176 | dlsmith@iso-ne.com